Tender documentation for the purchase of the spectroradiometer

Minimum requirements for technical parameters and parts of the supply:

- Wavelength range: 350 – 2500 nm

- Spectral resolution: less than 4 nm at 350 – 1000 nm, less than 30 nm at 1000 -2500 nm

- Sampling interval: less than 2 nm at 350 – 1000 nm, less than 8 nm at 1000 -2500 nm

- Min. scan speed: 100 miliseconds

- Possibility to connect an integration sphere

Price must include

- All additional equipment necessary for full instrument functionality

- Calibration (wavelength, reflectance, radiance)

- Shipping and insurance

- 2 years warranty

- Operating software

- User manual

- Spare battery

- Watertight protective hard case

Evaluation criteria

Total price without VAT		weighting factor 55 %

Technical parameters			weighting factor 30 %

Warranty, delivery and service		weighting factor   5 %

Shortening of shipment			weighting factor 10 %